Digital clock/date/thermometer with
PIC16F628/PIC16F84 and DS18S20/DS18B20
Flow chart
bogdi.ro/Bogdan Borca

---
Main
File: digital_cdt_pic16f84_628a_ds18sb20.asm
Start
Setup
;-- MAIN LOOP
;-- -------------------------------------------------
main
btfsc OPTIONS, 6	;-- test if a second elapsed/second event
goto second_event	;-- OPTIONS[6] is set in interrupt routine
back_from_int_second_event	;-- goto second event if yes
call test_keys	;-- test if set key was pressed
call TIME_LOOP	;-- write data
goto main	;-- keep running the main code.
Second event?
Second event
No
Set event?
Set event
No
Write data
to display

---
Setup
File: Inc\setup.inc
Variables/Registers:
Seconds [0..60]: kip track of time
sec_on_off [0,8]: if 0 dp lit, if 8 then dp don't lit
h [0..23]: hours
m [0..59]: minutes
dd [1..days/month]: date day
dm [1..12]: date month
year [0..99]: year from 2000 to 2099
OPTIONS:
[0] when user press the set button,
[1] is when user press + set button, OPTIONS[1]=1
[2] is when user press - set button, OPTIONS[2]=1
[3] is true when user pressed one of the +/- buttons
[4] set negative temperature flag: inside WW__WHAT is 3
[5] used by divide (divide is Done)
[6] second event reached
[7]=time (hh:mm) is displayed.. 1 for true 0 for false
tt [2..59]: time in seconds used to show the clock/time
td [0..59]: time in seconds used to show the date
te [0..59]: time in seconds used to show the temperature
date_type[1,2]: if 1 then letters are used, if 2 then numbers
WRT__CHG[1..tt/td/te]: time used to show current displayed data
WRT__WHAT[1..E(14)]:
1: display the time
2: display the date
3: display the temperature
4: display setting the hours (ho:[0..23])
5: display setting the minutes (nn:[0..59])
6: display setting the day of the month (dd:[1..d/m])
7: display setting the month (dn:[1..12])
8: display setting the year (dY:[0..99])
9: display setting date type (dt: [1,2])
10. (A) display setting time for time (tt:[2..99])
11. (B) display setting time for date (td:[0..99])
12. (C) display setting time for temperature (tE:[0..99])
13. (D) display setting SH (calibrate second high)
14. (E) display setting SL (calibrate second low)
goto setup
setup label
Initialize EE settings
Turn off comparator
Get EE settings
PORTA and PORTB
in/out setup
OPTIONS=10000000
Initialize days_per_month
Enable interrupts
WRT__CHG=tt
WRT__WHAT=1
seconds=0
sec_on_off=0
h=23
m=59
dd=31
dm=12
year=8
hold button
Initialize segments
with initialized data:
call test_WW
Request a DS18SB20
conversion
Initialize one
second event
variables:
bres_hi,
bres_mid
Goto
main

---
EE initialize/save/get settings

---
Second event
File: Inc\core.inc
Second event is triggered in interrupt routine by making OPTIONS[6]=true.
See interrupt routine below in the slides.
second_event
Clear OPTIONS[6]
Increment seconds
Seconds=60?
Call seconds_60
Decrement the time for
what is being displayed
WRT__CHG = WRT__CHG - 1
WRT__CHG=0?
Blink second
Search next available
data to display
Convert DS18SB20 if WRT__WHAT = 1
Read DS18SB20 if WRT__WHAT = 3
Return
Initialize segments
with new data:
call test_WW

---
Events
File: Inc\core.inc
Buttons +/- events are triggered when user presses set button
and they are handled by the test_keys call.
__what
Hold PORT button
unpressed to avoid multiple
execution on a single push
No
Return
hold=0?
Set mode already active?
OPTIONS[0]=1?
OPTIONS[0]=1
WRT__WHAT=3
seconds = 0
No
WRT__WHAT=WRT__WHAT + 1
hold=48
WRT__WHAT=
End of the settings?
Yes
Clear set mode
call SET_WRT__WHAT_to_1
Initialize segments
with new data:
call test_WW
Return
Blink second

---
Write data to display
File: Inc\core.inc
TL=4
call TIME_LOOP
TIME_LOOP
Write PORTA
and PORTB
Activate the TL
PORTA segment
Each segment is activated in an 4x255 us interval.
If TL is 3 then segment 3 is activated.
Segments are all connected to PORTA and activating
one of them means deactivating the others.
See Write PORTA and PORTB for further information.
Wait 4x255 us
hold = hold -1
TL=0?
No
Return
TL = TL - 1

---
Write PORTA and PORTB
File: Inc\core.inc
See test_WW and check how dig1 dig2 dig3 dig4 are initialized based on what
is being displayed.
write
Clear PORTA,
all segments are turned off
before writing to PORTB to
avoid flickering
PORTA=00011110 (1E)
W=20 (address of dig1)
W=W+TL
W=value from address(W)
Retrieve dig[1..4] address
using indirect addressing.
dig1, dig2, dig3 and dig4 are
initialized in test__WW and
they hold values needed to
be displayed
W=PORTB configuration
by calling put_number_in_W
The two middle points are located on PORTB[3] 0000X000
If we XOR PORTB with 0000A000 will make the X 1 if A=1 or 0 if A = 0.
Now think that sec_on_off has value of A value.
Get the configuration for PORTB to lit only necessary led:
W=put_number_in_W
EXAMPLE:
if W=0 before calling put_number_in_W then the first retlw
will return with the configuration place in W
=> retlw h'10' means
return in W: 00010000 what means that all led with 0 lit and all with 1 don't lit, in this case doesn't lit F led.
PORTB07=BAGF :DCE (from the display)
RB7=B RB6=A RB5=G RB4=F RB3=: RB2=D RB1=C RB0=E
XOR W with sec_on_off
(see wikipedia xor if
not familiar)
PORTB=W
Return/Back to
TIME_LOOP

---
Initialize segments with new data
File: Inc\options.inc
If WW_TEMP